## Slide 1: Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Topic 11.3 is an extension of Topics 5.1, 5.4, and 10.2.
Essential idea: Capacitors can be used to store electrical energy for later use.
Nature of science: Relationships: Examples of exponential growth and decay pervade the whole of science. It is a clear example of the way that scientists use mathematics to model reality. This topic can be used to create links between physics topics but also to uses in chemistry, biology, medicine and economics.
Notes: © 2015 by Timothy K. Lund

## Slide 2
Understandings:
• Capacitance
• Dielectric materials
• Capacitors in series and parallel
• Resistor-capacitor (RC) series circuits
• Time constant
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 2
© 2015 by Timothy K. Lund

## Slide 3
Applications and skills:
• Describing the effect of different dielectric materials on capacitance
• Solving problems involving parallel-plate capacitors
• Investigating combinations of capacitors in series or parallel circuits
• Determining the energy stored in a charged capacitor
• Describing the nature of the exponential discharge of a capacitor
• Solving problems involving the discharge of a capacitor through a fixed resistor
• Solving problems involving the time constant of an RC circuit for charge, voltage and current
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 3
© 2015 by Timothy K. Lund

## Slide 4
Guidance:
• Only single parallel-plate capacitors providing a uniform electric field, in series with a load, need to be considered (edge effect will be neglected)
• Problems involving the discharge of capacitors through fixed resistors need to be treated both graphically and algebraically
• Problems involving the charging of a capacitor will only be treated graphically
• Derivation of the charge, voltage and current equations as a function of time is not required
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 4
© 2015 by Timothy K. Lund

## Slide 5
Data booklet reference:
•
•
•
•
•
•
•
•
•
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 5
© 2015 by Timothy K. Lund

## Slide 6
International-mindedness:
• Lightning is a phenomenon that has fascinated physicists from Pliny through Newton to Franklin. The charged clouds form one plate of a capacitor with other clouds or Earth forming the second plate. The frequency of lightning strikes varies globally, being particularly prevalent in equatorial regions. The impact of lightning strikes is significant with many humans and animals being killed annually and huge financial costs to industry from damage to buildings, communication and power transmission systems, and delays or the need to reroute air transport.
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 6
© 2015 by Timothy K. Lund

## Slide 7
Utilization:
• The charge and discharge of capacitors obeys rules that have parallels in other branches of physics including radioactivity (see Physics sub-topic 7.1)
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 7
© 2015 by Timothy K. Lund

## Slide 8
Aims:
• Aim 3: the treatment of exponential growth and decay by graphical and algebraic methods offers both the visual and rigorous approach so often characteristic of science and technology
• Aim 6: experiments could include (but are not limited to): investigating basic RC circuits; using a capacitor in a bridge circuit; examining other types of capacitors; verifying time constant Essential idea: Generation and transmission of alternating current (ac) electricity has transformed the world.
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 8
© 2015 by Timothy K. Lund

## Slide 9
Capacitance
A capacitor is an electronic device that stores charge.
In its simplest form, it is made up of two separated parallel plates. In between the plates we can have air, vacuum, or a non-conductive material called a dielectric.
Although there are other types of capacitors, in this topic we will study the parallel plate capacitor. Its schematic is shown here, and is comprised of two parallel lines.
An electrolytic capacitor has a higher capacity than a parallel plate capacitor.
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 9
© 2015 by Timothy K. Lund

## Slide 10
FYI
Don’t confuse (capacitance) with C (Coulombs).
EXAMPLE: A 1.50-V cell is connected to a 275 F capacitor in the circuit shown. How much charge is stored on the capacitor’s plates?
SOLUTION: Use  .
= = 27510-61.50 = 4.13 10-4 C.
Capacitance
We define the capacitance C to be the charge q per unit voltage V which the capacitor is capable of maintaining.
The units for capacitance are Coulombs per volt which are called farads and abbreviated F.
definition of capacitance
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 10
© 2015 by Timothy K. Lund

## Slide 11
Capacitance – parallel
Just as we connected resistors in parallel, so too can we connect capacitors.
Because the capacitors are in parallel, they each have the cell’s voltage V.
Thus V = V1 = V2.
From C = we get q = CV. Thus
q = CV, q1 = C1V1 , and q2 = C2V2.
Conservation of charge tells us that q = q1 + q2:
CV = C1V1 + C2V2
CV = C1V + C2V
C = C1 + C2
C = C1 + C2 + …
parallel capacitance
a variable capacitor takes advantage of many parallel plates…
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
V
C1
C2
Notes: 11
© 2015 by Timothy K. Lund

## Slide 12
EXAMPLE: A 1.50-V cell is connected to C1 = 275 F and C2 = 38 F in the circuit.
(a) What value should a single replacement capacitor have?
SOLUTION: The capacitors are in parallel.
C = C1 + C2 = 27510-6 + 3810-6
= 31310-6 F.
(b) How much charge has the battery placed on the capacitors?
SOLUTION:
q = CV = 31310-61.50
= 47010-6 C.
Capacitance – parallel
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
V
C1
C2
Notes: 12
© 2015 by Timothy K. Lund

## Slide 13
FYI Note that the series/parallel formulas for capacitance are reversed from those for resistance!
Capacitance – series
We can also connect capacitors in series:
Because the capacitors are in series, they each have the same charge .
Thus .
From we get . Thus
, , and .
Conservation of energy tells us that so that
V
C1
C2
series capacitance
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 13
© 2015 by Timothy K. Lund

## Slide 14
EXAMPLE: A 1.50-V cell is connected to C1 = 275F and C2 = 38 F in the circuit.
(a) What value should a single replacement capacitor have?
SOLUTION: The capacitors are in series.
.
F.
(b) How much charge has the battery placed on each capacitor? What are their voltages?
SOLUTION: Series capacitors have the same charge.
C.
V.
V.
Capacitance – series
Note that VCi = V.
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
V
C1
C2
Notes: 14
© 2015 by Timothy K. Lund

## Slide 15
Dielectric materials
A simple capacitor consists of two conductors separated by non-conductive space.
Thus, even the wires in an electronic circuit have capacitance. In extremely high frequency circuits this inter-wire capacitance may cause problems and must be minimized through proper design.
Capacitors are, however, used in most electronics devices, and large capacity in small space is the premium.
Capacitors are used as filters, coupling devices, voltage smoothing (as in the full-wave rectifier), and timing devices.
+ + + + + +
– – – – – –
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 15
© 2015 by Timothy K. Lund

## Slide 16
Dielectric materials
When capacitance is desired, large capacity in a small space is the premium.
In order to increase the ability of a capacitor to store charge, we use conductive plates instead of wires.
There are two ways to increase the capacitance.
1: Increase the area over which charge can be stored (thus the like charges can “spread out” and chill in their own personal space).
2: Decrease the distance between the plates (thus the charges on the opposite plates attract even more to each other, making it easier for the cell to “pump” charge into the device).
A
d
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 16
© 2015 by Timothy K. Lund

## Slide 17
Dielectric materials
Because the attractive force between charges is, by Coulomb’s law, , we see that it grows quadratically with decreasing plate separation d.
Charge leakage can occur through air or vacuum. So what manufacturers do is they place a non-conductive material called a dielectric between the plates. This will both reduce arcing and the electric force, increasing the capacity of the capacitor.
The epsilon  is the permittivity of the dielectric. Recall that the permittivity of free space (and air) is 0 = 8.8510-12 F m-1.
parallel-plate capacitor
dielectric
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 17
© 2015 by Timothy K. Lund

## Slide 18
Dielectric materials
What a dielectric material does is it essentially reduces the electric field by the ratio .
The way it does this is that the molecules in the dielectric material are polarized in response to the electric field of the plates, and create an oppositely-oriented electric field.
This dielectric field cancels some of the original field, thereby diminishing the overall E-field between the plates.
From and recalling from 10.2 that , we see that so that . This tells us that the smaller the electric field is, the larger the capacitance.
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 18
© 2015 by Timothy K. Lund

## Slide 19
EXAMPLE: A 275 F capacitor will be manufactured using a dielectric having a permittivity of 4.000 and circular plates having a diameter of 2.50 cm. What should the plate separation (and the thickness of the dielectric) be? Is it likely that this large a capacity could be constructed using parallel plate architecture?
SOLUTION: Use .
The area in the formula is the area of one plate.
m2.
m.
Given that the plate separation is of the order of an atomic diameter, it is very unlikely that one could construct a 275 F parallel plate capacitor.
Dielectric materials
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 19
© 2015 by Timothy K. Lund

## Slide 20
Energy stored in a capacitor
From the relationship we can write .
We see, then, that the graph of V vs. q is a straight line having a slope of :
Recall that the work done by a cell is given by , provided and are constant. If they are not constant, = area under the vs. graph.
Since the area of a triangle is we have .
From conservation of energy, this is then the energy stored in a capacitor.
V
q
energy stored in a capacitor
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 20
© 2015 by Timothy K. Lund

## Slide 21
PRACTICE: On the previous slide it was shown that the energy stored in a capacitor is E = ½qV. Show that the energy stored in a capacitor is also given by E = ½CV 2. Then, find the energy stored in a 275 F capacitor charged up to 1.50 V.
SOLUTION:
Use the definition of capacitance .
Then so that
.
Finally,
J.
Energy stored in a capacitor
E = ½qV = ½CV 2
energy stored in a capacitor
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 21
© 2015 by Timothy K. Lund

## Slide 22
EXAMPLE: Two capacitors are in the circuit shown. C1 is fully charged at 1.50 V, and C2 is initially uncharged.
What is the electrical energy stored in C1?
(b) What is the charge on C1’s plates?
SOLUTION:
(a) J (see previous slide).
(b) C.
Solving problems involving parallel-plate capacitors
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 22
© 2015 by Timothy K. Lund

## Slide 23
EXAMPLE: Continued…
(c) When the switch is closed, what will the charge on C1 be? What charge will C2 have?
SOLUTION: The capacitors are in parallel. Thus
.
Thus .
From conservation of charge, C.
C.
Solving problems involving parallel-plate capacitors
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
C.
Notes: 23
© 2015 by Timothy K. Lund

## Slide 24
EXAMPLE: A capacitor having no dielectric has a capacitance of 325 pF. It is charged up to 6.00 V by momentarily attaching it to a battery, and then disconnecting it.
(a) What is the energy stored in the capacitor at this voltage?
(b) What is the charge on the capacitor?
SOLUTION:
(a) J.
(b) C.
Solving problems involving parallel-plate capacitors
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 24
© 2015 by Timothy K. Lund

## Slide 25
EXAMPLE: A capacitor having no dielectric has a capacitance of 325 pF. It is charged up to 6.00 V by momentarily attaching it to a battery, and then disconnecting it.
(c) A dielectric having a permittivity of 20 is now carefully inserted between the plates of the capacitor. What is its new capacitance?
SOLUTION: Use .
(c) and so that
. pF.
Solving problems involving parallel-plate capacitors
dielectric
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 25
© 2015 by Timothy K. Lund

## Slide 26
EXAMPLE: A capacitor having no dielectric has a capacitance of 325 pF. It is charged up to 6.00 V by momentarily attaching it to a battery, and then disconnecting it.
(d) What is the charge on the new capacitor?
(e) What is the voltage on the new capacitor?
SOLUTION:
(d) The charge does not change. Why?
Thus C.
(e) From we see that
V.
Solving problems involving parallel-plate capacitors
dielectric
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Conservation of charge.
Notes: 26
© 2015 by Timothy K. Lund

## Slide 27
EXAMPLE: Continued…
(f) What is the energy stored in the new capacitor?
(g) Explain the discrepancy between (f) and (a).
SOLUTION:
(f) Use either or :
J.
(g) This is half the energy stored in the capacitor without the dielectric. The dielectric would be attracted into the void: The “inserter” would have to do negative work!
Solving problems involving parallel-plate capacitors
dielectric
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 27
© 2015 by Timothy K. Lund

## Slide 28
Charge can be neither created nor destroyed.
It can be separated into (+) and (-) in equal quantities.
The (-) was separated from the ground, leaving behind an equal amount of (+).
+ + + + + + + + + + + + + + +
Solving problems involving parallel-plate capacitors
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: © 2015 by Timothy K. Lund

## Slide 29
+ + + + + + + + + + + + + + +
The electric field strength E at any point in space is equal to the force per unit charge at that point.
If in doubt, find the applicable formula and translate it into words. “E = F / q.”
Solving problems involving parallel-plate capacitors
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: © 2015 by Timothy K. Lund

## Slide 30
+ + + + + + + + + + + + + + +
Just recall that between parallel plates the E-field is uniform (equally spaced), and it points from (+) toward (-).
Solving problems involving parallel-plate capacitors
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: © 2015 by Timothy K. Lund

## Slide 31
C m-2.
0 = 8.85×10-12 C2 N-1 m−2 (from Data Booklet).
Then Vm-1.
Solving problems involving parallel-plate capacitors
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: © 2015 by Timothy K. Lund

## Slide 32
 is the same everywhere on the cloud.
0 is the same in air as in free space.
The ground and the cloud’s lower surface are flat and parallel.
Solving problems involving parallel-plate capacitors
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: © 2015 by Timothy K. Lund

## Slide 33
Use and ignore the sign:
Then ∆V = E ∆r = (3×105)(500) = 1.5108 V!
Solving problems involving parallel-plate capacitors
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: © 2015 by Timothy K. Lund

## Slide 34
Solving problems involving parallel-plate capacitors
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
A.
J.
Or… W.
J.
Notes: © 2015 by Timothy K. Lund

## Slide 35
PRACTICE: A 1.50-V cell is connected to a 275 F capacitor in the circuit shown.
(a) Make a sketch graph of what the voltmeter reads after the switch is closed.
SOLUTION:
Before the switch is closed the voltage on the capacitor is zero.
After the switch is closed, the voltage will increase from zero to 1.50 V in a very short amount of time as the plates store the charge.
Then the capacitor’s voltage will remain at 1.50 V.
Charging a capacitor
V / V
t
1.50
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 35
© 2015 by Timothy K. Lund

## Slide 36
PRACTICE: A 1.50-V cell is connected to a 275 F capacitor in the circuit shown.
(b) Make a sketch graph of what the ammeter reads after the switch is closed.
SOLUTION:
Before the switch is closed the current is zero.
After the switch is closed, the current will begin at a maximum value and will decrease rapidly as the plates “fill up” with charge and repel further charge.
Then the current will remain at zero.
Charging a capacitor
I / A
t
MAX
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 36
© 2015 by Timothy K. Lund

## Slide 37
PRACTICE: A 1.50-V cell is connected to a 275 F capacitor in the circuit shown.
(c) Make a sketch graph of the charge q on the plates after the switch is closed.
SOLUTION:
Before the switch is closed the charge is zero.
After the switch is closed, the charge will rapidly “fill up” the plates and slow down the subsequent flow due to repulsion.
Then the charge will reach a maximum value on the plates, stopping the flow of further charge.
Charging a capacitor
q / C
t
MAX
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 37
© 2015 by Timothy K. Lund

## Slide 38
PRACTICE: A 1.50-V cell is connected in series to a capacitor and resistor.
Make a sketch graph showing the family of curves representing the voltage across the resistor after the switch is closed as RC increases.
SOLUTION:
Before the switch is closed the current is zero.
After the switch is closed, the current will begin at a maximum value and will decrease rapidly as the plates “fill up” with charge and repel further charge.
Then the current will remain at zero.
RC series circuits – charging
I / A
t
MAX
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
C
R
Notes: 38
© 2015 by Timothy K. Lund

## Slide 39
PRACTICE: A 1.50-V cell is connected in series to a capacitor and resistor.
Make a sketch graph showing the family of curves representing the voltage across the resistor after the switch is closed as RC increases.
SOLUTION:
Because the voltage across the resistor is proportional to the current (V = IR), its graph will have the same shape as I:
Furthermore, the bigger R and C are, the longer it will take for the capacitor to charge and the current to stop.
RC series circuits – charging
I / A
t
MAX
V / V
t
1.50
low RC
medium RC
high RC
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
C
R
Notes: 39
© 2015 by Timothy K. Lund

## Slide 40
PRACTICE: A two-position switch can alternately charge (A) and discharge (B) a capacitor C through a resistor R.
Make sketch graphs of what the charge across the capacitor C reads when the switch is placed (a) at position A, and (b) at position B.
SOLUTION:
(a) When the switch is placed at A the circuit is connected to the cell and thus begins to charge.
(b) When the switch is then placed at B, the capacitor begins to discharge through the wire and the resistor.
RC series circuits – discharging
q / Q
t
q0
q / C
t
q0
switch in position A to charge
switch in position B to discharge
C
R
A
B
+
–
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 40
© 2015 by Timothy K. Lund

## Slide 41
RC series circuits – discharging
Suppose the capacitor is fully charged.
Then we place the switch to position B for discharge:
The (+) on the top plate then travels CW through the wire and the resistor to the bottom plate:
If we use Kirchhoff’s rule for V we see that following the loop in the direction of the current we have
.
But since and since we have
.
The (–) sign on the right hand side shows that q is ALWAYS negative during discharge.
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
C
R
A
B
+
–
Notes: 41
© 2015 by Timothy K. Lund

## Slide 42
FYI
Many of the formulas we use in IB physics are easily derived using both differential and integral calculus. Although IB requires you to use the resulting formulaic solutions to the differential equations, you do not have to derive them.
RC series circuits – discharging
We can write the results of the RC discharge thus:
As an aside, and beyond the scope of this course, the exponential form comes from the associated differential equation: . It turns out that is its time-dependent solution.
RC discharge
where  = RC
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 42
© 2015 by Timothy K. Lund

## Slide 43
EXAMPLE: A 275 F capacitor is charged to 6.00 V. It is then discharged through a 10.0 M resistor.
(a) Find the time constant.
(b) Find the initial charge on the plates.
SOLUTION:
(a) The time constant is  = RC.
s.
(b) C.
RC series circuits – discharging
We call  = RC the time constant, and see that it has the units of seconds (time).
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
RC discharge
where  = RC
Notes: 43
© 2015 by Timothy K. Lund

## Slide 44
EXAMPLE: A 275 F capacitor is charged to 6.00 V. It is then discharged through a 10.0 M resistor.
(c) Find the charge on the plates exactly one time constant after discharge has begun.
SOLUTION:
(c) Substitute and C into .
C.
This is 37% of its original charge.
RC series circuits – discharging
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
RC discharge
where  = RC
Notes: 44
© 2015 by Timothy K. Lund

## Slide 45
FYI
The IBO does not require you to know the charging formulae. You only need to make sketch graphs.
RC series circuits – discharging
Because of the relationships and we can derive the next two formulas easily:
Keep in mind that is the voltage across the capacitor and not the resistor. The resistor will have a starting voltage of zero. Kirchhoff’s rule for V would produce the resistor voltage formula
RC discharge
where
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
RC discharge
where  = RC
Notes: 45
© 2015 by Timothy K. Lund

## Slide 46
EXAMPLE: A 275 F capacitor is charged to 6.00 V. It is then discharged through a 10.0 M resistor. Find the average current during the first 1375 s of discharge.
SOLUTION: Use q0 = 0.00165 C, and  = 2750 s.
Substitute t = 0 and t = 1375 into q = q0 e -t / .
C
C
A.
RC series circuits – discharging
Ignore the (–) sign.
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
RC discharge
where  = RC
Notes: 46
© 2015 by Timothy K. Lund

## Slide 47
EXAMPLE: A 275 F capacitor is charged to 6.00 V. It is then discharged through a 10.0 M resistor. Find the instantaneous current at t = 1375 s.
SOLUTION: Use q0 = 0.00165 C, and  = 2750 s.
Substitute t = 1375 s into .
C
A.
RC series circuits – discharging
Ignore the (–) sign.
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
RC discharge
where  = RC
Notes: 47
© 2015 by Timothy K. Lund

## Slide 48
PRACTICE: A 275 F capacitor is charged to 6.00 V. It is then discharged through a 10.0 M resistor. Find the instantaneous voltage at t = 1375 s. Then find the instantaneous current using Ohm’s law.
SOLUTION: Use q0 = 0.00165 C, and  = 2750 s.
Substitute t = 1375 s into .
V.
A.
RC series circuits – discharging
Note that this is the same answer as we got on the previous slide.
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
RC discharge
where
Notes: 48
© 2015 by Timothy K. Lund

## Slide 49
RC series circuits – discharging
Suppose we want to find the “half-life” of a charged capacitor (when its voltage/charge/current will have decayed to half its original value).
Substitute into .
.
ln ln
half-life
T1/2 =  ln 2
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 49
© 2015 by Timothy K. Lund

## Slide 50
PRACTICE: A timer using a capacitor and a resistor needs the RC circuit to have a half-life of 2500 seconds. It will be using a capacitor of 275 F. What value should the resistor have?
SOLUTION:
Substitute T1/2 = 2500 s into T1/2 =  ln 2.
s.
But . Thus
 ( M).
RC series circuits – discharging
half-life
T1/2 =  ln 2
Topic 11: Electromagnetic induction - AHL 11.3 – Capacitance
Notes: 50
© 2015 by Timothy K. Lund