## Slide 1: Topic 2: Mechanics 2.2 – Forces
Essential idea: Classical physics requires a force to change a state of motion, as suggested by Newton in his laws of motion.
Nature of science: (1) Using mathematics: Isaac Newton provided the basis for much of our understanding of forces and motion by formalizing the previous work of scientists through the application of mathematics by inventing calculus to assist with this. (2) Intuition: The tale of the falling apple describes simply one of the many flashes of intuition that went into the publication of Philosophiæ Naturalis Principia Mathematica in 1687.
Notes: © 2006 By Timothy K. Lund

## Slide 2: Topic 2: Mechanics 2.2 – Forces
Understandings:
• Objects as point particles
• Free-body diagrams
• Translational equilibrium
• Newton’s laws of motion
• Solid friction
Notes: 2
© 2006 By Timothy K. Lund

## Slide 3: Topic 2: Mechanics 2.2 – Forces
Applications and skills:
• Representing forces as vectors
• Sketching and interpreting free-body diagrams
• Describing the consequences of Newton’s first law for translational equilibrium
• Using Newton’s second law quantitatively and qualitatively
• Identifying force pairs in the context of Newton’s third law
• Solving problems involving forces and determining resultant force
• Describing solid friction (static and dynamic) by coefficients of friction
Notes: 3
© 2006 By Timothy K. Lund

## Slide 4: Topic 2: Mechanics 2.2 – Forces
Guidance:
• Students should label forces using commonly accepted names or symbols (for example: weight or force of gravity or mg)
• Free-body diagrams should show scaled vector lengths acting from the point of application
• Examples and questions will be limited to constant mass
• mg should be identified as weight
• Calculations relating to the determination of resultant forces will be restricted to one- and two-dimensional situations
Notes: 4
© 2006 By Timothy K. Lund

## Slide 5: Topic 2: Mechanics 2.2 – Forces
Data booklet reference:
• F = ma
• Ff ≤ µsR
• Ff = µdR
Theory of knowledge:
• Classical physics believed that the whole of the future of the universe could be predicted from knowledge of the present state. To what extent can knowledge of the present give us knowledge of the future?
Notes: 5
© 2006 By Timothy K. Lund

## Slide 6: Topic 2: Mechanics 2.2 – Forces
Utilization:
• Motion of charged particles in fields (see Physics sub-topics 5.4, 6.1, 11.1, 12.2)
• Application of friction in circular motion (see Physics sub-topic 6.1)
• Construction (considering ancient and modern approaches to safety, longevity and consideration of local weather and geological influences)
• Biomechanics (see Sports, exercise and health science SL sub-topic 4.3)
Notes: 6
© 2006 By Timothy K. Lund

## Slide 7: Topic 2: Mechanics 2.2 – Forces
Aims:
• Aims 2 and 3: Newton’s work is often described by the quote from a letter he wrote to his rival, Robert Hooke, which states: “What Descartes did was a good step. You have added much [in] several ways. If I have seen a little further it is by standing on the shoulders of Giants.” This quote is also inspired, this time by writers who had been using versions of it for at least 500 years before Newton’s time.
• Aim 6: experiments could include (but are not limited to): verification of Newton’s second law; investigating forces in equilibrium; determination of the effects of friction.
Notes: 7
© 2006 By Timothy K. Lund

## Slide 8: Topic 2: Mechanics 2.2 – Forces
Representing forces as vectors
A ______ is a ____________ measured in _________.
One force we are very familiar with is the force of gravity, also known as the _______.
The very concepts of push and pull imply direction. Thus ______________________.
The direction of the weight is ______ toward the center of the earth.
If you have a weight of 90 Newtons (or 90 N), your weight can be expressed as a vector: 90 N, down.
We will show later that weight has the formula
weight
where g = -9.8 m s -2
and m is the mass in kg
Notes: © 2006 By Timothy K. Lund

## Slide 9: Topic 2: Mechanics 2.2 – Forces
Newton’s laws of motion – The first law
Newton’s first law is related to certain studies made by Galileo Galilee which contradicted Aristotelian tenets.
Aristotle basically said “The natural state of motion of all objects (but the heavenly ones) is one of rest.”
A child will learn that if you stop pushing a wagon, the wagon will eventually stop moving.
This simple observation will lead the child to come up with a force law that looks something like this:
“In order for a body to be in motion, there must be a force acting on it.”
As we will show on the next slide, both of these observations are false!
Notes: © 2006 By Timothy K. Lund

## Slide 10: Topic 2: Mechanics 2.2 – Forces
Newton’s laws of motion – The first law
Here’s how Galileo (1564-1642) thought:
If I give a cart a push on a smooth, level surface, it will eventually stop.
What can I do to increase the distance it rolls without pushing it harder or changing the slope?
If I can minimize the friction, it’ll go farther.
In fact, he reasoned, if I eliminate the friction altogether the cart will roll forever!
Galileo called the tendency of an object to not change its state of motion _________.
Inertia will only change if there is a force.
Notes: © 2006 By Timothy K. Lund

## Slide 11: Topic 2: Mechanics 2.2 – Forces
Describing the consequences of Newton’s first law for translational equilibrium
Newton’s first law is drawn from his concept of net force and Galileo’s concept of inertia.
Newton’s first law says that _____________________ ____________________________________________.
In his words...“Every body continues in its state of rest, or of uniform motion in a straight line, unless it is compelled to change that state by forces impressed thereon.”
In symbols...
____________________________________________
Newton’s first law
A body’s velocity will only change if there is a net force acting on it.
Notes: © 2006 By Timothy K. Lund

## Slide 12: Topic 2: Mechanics 2.2 – Forces
Translational equilibrium
As a memorable demonstration of inertia – matter’s tendency to not change its state of motion (or its state of rest) - consider this:
A water balloon is cut very rapidly with a knife.
For an instant the water remains at rest!
Notes: © 2006 By Timothy K. Lund

## Slide 13: Topic 2: Mechanics 2.2 – Forces
Free-body diagram
Objects as point particles and Free-body diagrams
EXAMPLE: Calculate the weight of a 25-kg object.
SOLUTION:
Since m = 25 kg and g = -9.8 m s-2,
Note that ___________________ from the fact that ______________.
We sketch the mass as a ____________(dot), and the __________________ in a __________ _______________:
W = mg
weight
where g = -9.8 m s -2
and m is the mass in kg
Notes: © 2006 By Timothy K. Lund

## Slide 14: Topic 2: Mechanics 2.2 – Forces
Objects as point particles and Free-body diagrams
Certainly there are other forces besides weight that you are familiar with.
For example, when you set a mass on a tabletop, even though it stops moving, it still has a weight.
The implication is that the tabletop applies a __________ to the weight, called a ____________.
Note that the weight and the normal forces are the same length – they ___________.
The __________ is called a _________________
W
N
Notes: © 2006 By Timothy K. Lund

## Slide 15: Topic 2: Mechanics 2.2 – Forces
Objects as point particles and Free-body diagrams
_____________ T can only be a pull and never a push.
___________ Ff tries to oppose the motion.
___________ Ff is _______________________________.
__________ N is ________________________________.
Friction and normal are mutually ______________. Ff N.
Friction and normal are __________________________.
_______ W is an ________________________________.
T
the tension
W
N
Ff
Contact surface
Notes: © 2006 By Timothy K. Lund

## Slide 16: Topic 2: Mechanics 2.2 – Forces
Sketching and interpreting free-body diagrams
Weight is sketched from the center of an object.
Normal is always sketched perpendicular to the contact surface.
Friction is sketched parallel to the contact surface.
Tension is sketched at whatever angle is given.
Notes: © 2006 By Timothy K. Lund

## Slide 17: Topic 2: Mechanics 2.2 – Forces
EXAMPLE: An object has a tension acting on it at 30° as shown. Sketch in the forces, and draw a free-body diagram.
SOLUTION:
Free-body diagram
Sketching and interpreting free-body diagrams
T
30°
Notes: © 2006 By Timothy K. Lund

## Slide 18: Topic 2: Mechanics 2.2 – Forces
Solving problems involving forces and resultant force
The ___________________ is just the ____________ ___________________________________.
EXAMPLE: An object has mass of 25 kg. A tension of 50 N and a friction force of 30 N are acting on it as shown. What is the resultant force?
SOLUTION:
Since the weight and the normal forces cancel out in the y-direction, we only need to worry about the forces in the x-direction.
T
W
N
Ff
50 N
30 N
Notes: © 2006 By Timothy K. Lund

## Slide 19: Topic 2: Mechanics 2.2 – Forces
Solving problems involving forces and resultant force
The resultant (or net) force is just the vector sum of all of the forces acting on a body.
EXAMPLE: An object has exactly two forces F1 = 50. N and F2 = 30. N applied simultaneously to it. What is the resultant force’s magnitude?
SOLUTION:
Fnet = F = F1 + F2 so we simply graphically add the two vectors:
F1
50. N
F2
30. N
net force
Notes: © 2006 By Timothy K. Lund

## Slide 20: Topic 2: Mechanics 2.2 – Forces
Solving problems involving forces and resultant force
The resultant (or net) force is just the vector sum of all of the forces acting on a body.
EXAMPLE: An object has exactly two forces F1 = 50. n and F2 = 30. n applied simultaneously to it as shown. What is the resultant force’s direction?
SOLUTION:
Direction is measured from the (+) x-axis.
Opposite and adjacent are given directly, so use tangent.
F1
50. N
F2
30. N
Fnet

Fnet = F
net force
Fx,net = Fx
Fy,net = Fy
Notes: © 2006 By Timothy K. Lund

## Slide 21: Topic 2: Mechanics 2.2 – Forces
EXAMPLE: An object has exactly two forces F1 = 50. N and F2 = 30. N applied simultaneously to it. What is the resultant force’s magnitude?
SOLUTION:
Begin by resolving F1 into its x- and y-components.
Then Fnet,x =
Fnet,y =
Fnet2 = Fnet,x2 + Fnet,y2
Solving problems involving forces and resultant force
F1
50. N
F2
30. N
28°
Notes: © 2006 By Timothy K. Lund

## Slide 22: Topic 2: Mechanics 2.2 – Forces
Translational equilibrium
EXAMPLE: An object of mass m is hanging via three cords as shown. Find the tension in each of the three cords, in terms of m.
SOLUTION:
Give each tension a name to organize your effort.
Draw a free body diagram of the mass and the knot.
T3 is the easiest force to find. Why?
Since m is not moving, its FBD tells us that
Fy = 0.
knot
30°
45°
T1
T2
T3
mg
FBD, m
FBD, knot
m
Notes: © 2006 By Timothy K. Lund

## Slide 23: Topic 2: Mechanics 2.2 – Forces
EXAMPLE: An object of mass m is hanging via three cords as shown. Find the tension in each of the three cords, in terms of m.
SOLUTION: T3 = mg
Now we break T1 and T2 down to components.
Looking at the FBD of the knot we see that
T1x = =
T1y = =
T2x = =
T2y = =
mg
T3
FBD, m
FBD, knot
T2
T1
T3
30°
45°
Translational equilibrium
knot
30°
45°
T1
T2
T3
m
Notes: © 2006 By Timothy K. Lund

## Slide 24: Topic 2: Mechanics 2.2 – Forces
Translational equilibrium
EXAMPLE: An object of mass m is hanging via three cords as shown. Find the tension in each of the three cords, in terms of m.
SOLUTION: T3 = mg
∑Fx = 0
∑Fy = 0
mg
T3
FBD, m
FBD, knot
T2
T1
T3
30°
45°
knot
30°
45°
T1
T2
T3
m
Notes: © 2006 By Timothy K. Lund

## Slide 25: Topic 2: Mechanics 2.2 – Forces
Solving problems involving forces and resultant force
PRACTICE: A 25-kg mass is hanging via three cords as shown. Find the tension in each of the three cords, in Newtons.
SOLUTION:
Since all of the angles are the same use the formulas we just derived:
FYI This was an example of using Newton’s first law with v = 0. The next example shows how to use Newton’s first law when v is constant, but not zero.
knot
30°
45°
T1
T2
T3
m
Notes: © 2006 By Timothy K. Lund

## Slide 26: Topic 2: Mechanics 2.2 – Forces
Solving problems involving forces and resultant force
EXAMPLE: A 1000. kg airplane is flying at a constant velocity of 125 m s-1. Label and determine the value of the weight W, the lift L, the drag D and the thrust F if the drag is 25000 N.
SOLUTION:
Since the velocity is constant, Newton’s first law applies. Thus Fx = 0 and Fy = 0.
W
L
D
F
Notes: © 2006 By Timothy K. Lund

## Slide 27: Topic 2: Mechanics 2.2 – Forces
Newton’s laws of motion – The second law
Newton reasoned: ____________________________ ____________________________________
Newton knew (as we also know) that a change in velocity is an acceleration.
So Newton then asked himself: “How is the sum of the forces related to the acceleration?”
Here is what Newton said: ______________________ ____________________________________________ ____________________________________________
The bigger the force the bigger the acceleration, and the bigger the mass the smaller the acceleration.
Newton’s second law
Notes: © 2006 By Timothy K. Lund

## Slide 28: Topic 2: Mechanics 2.2 – Forces
Newton’s laws of motion – The second law
Looking at the form F = ma note that
__________________________.
But if _______________________________.
Thus Newton’s first law is just a special case of his second – namely, when the acceleration is zero.
Fnet = ma
Newton’s second law
(or F = ma )
FYI
The condition ______ can is thus the _____________ ___________________________, just as ________ is.
Notes: © 2006 By Timothy K. Lund

## Slide 29: Topic 2: Mechanics 2.2 – Forces
Newton’s laws of motion – The second law
EXAMPLE: An object has a mass of 25 kg. A tension of 50 N and a friction force of 30 N are acting on it as shown. What is its acceleration?
SOLUTION:
The vertical forces W and N cancel out.
The net force is thus
From Fnet = ma we get:
so that:
T
W
N
Ff
50 N
30 N
Fnet = ma
Newton’s second law
(or F = ma )
Notes: © 2006 By Timothy K. Lund

## Slide 30: Topic 2: Mechanics 2.2 – Forces
Newton’s laws of motion – The second law
Fnet = ma
Newton’s second law
(or F = ma )
PRACTICE: Use F = ma to show that the formula for weight is correct.
SOLUTION:
Notes: © 2006 By Timothy K. Lund

## Slide 31: Topic 2: Mechanics 2.2 – Forces
Newton’s laws of motion – The second law
Fnet = ma
Newton’s second law
(or F = ma )
EXAMPLE: A 1000-kg airplane is flying in perfectly level flight. The drag D is 25000N and the thrust F is 40000N. Find its acceleration.
SOLUTION:
Since the flight is level, _______.
Fx =
W
L
D
F
Notes: © 2006 By Timothy K. Lund

## Slide 32: Topic 2: Mechanics 2.2 – Forces
Solving problems involving forces and resultant force
EXAMPLE: A 25-kg object has exactly two forces
F1 = 40. N and F2 = 30. N applied simultaneously to it. What is the object’s acceleration?
SOLUTION:
Resolve F1 into its components:
F1
F2
30 N
25°
Notes: © 2006 By Timothy K. Lund

## Slide 33: Topic 2: Mechanics 2.2 – Forces
Solving problems involving forces and resultant force
EXAMPLE: A 25-kg object resting on a frictionless incline is released, as shown. What is its acceleration?
SOLUTION:
Begin with a FBD.
Break down the weight into its components.
Since N and mg cos 30°are perpendicular to the path of the crate they do NOT contribute to its acceleration.
Thus
30°
6.0 m
Notes: © 2006 By Timothy K. Lund

## Slide 34: Topic 2: Mechanics 2.2 – Forces
Solving problems involving forces and resultant force
EXAMPLE: A 25-kg object resting on a frictionless incline is released, as shown. What is its speed at the bottom?
SOLUTION:
We found that its acceleration is 4.9 m s-2.
We will __________________ to find , so we need s.
We have opposite and we want hypotenuse s so from trigonometry, we use sin  = .
Thus
30°
6.0 m
s
a = 4.9 m s-2
Notes: © 2006 By Timothy K. Lund

## Slide 35
Solid friction
Recall that __________________________________ ______________, and _________________________.
Suppose we begin to pull a crate to the right, with gradually increasing force.
We plot the applied force, and the friction force, as functions of time:
T
f
T
f
T
f
T
f
T
f
Force
Time
tension
friction
static
friction
dynamic
friction
static
dynamic
Topic 2: Mechanics 2.2 – Forces
Notes: © 2006 By Timothy K. Lund

## Slide 36
Solid friction
During the static phase, the _________________ Fs exactly ____________ ____________________.
_________________until it reaches a maximum value Fs,max.
The friction force then almost ____________________ _______________________, called the ____________ ______________________.
Take note of the following general properties of the friction force:
Force
Time
tension
friction
static
dynamic
Fs,max
Fd
Topic 2: Mechanics 2.2 – Forces
Notes: © 2006 By Timothy K. Lund

## Slide 37
Describing solid friction by coefficients of friction
Since there are two types of friction, static and dynamic, ____________________________________ ____________________________________.
In addition to the "roughness" or "smoothness" of the materials, the friction force _________, not surprisingly, _________________________.
The harder the two surfaces are squished together (this is what the normal force measures) the more friction there will be.
Here are the relationships between the friction force Ff, the coefficients of friction μ, and the normal force N:
Topic 2: Mechanics 2.2 – Forces
friction
static
dynamic
Notes: © 2006 By Timothy K. Lund

## Slide 38
Topic 2: Mechanics 2.2 – Forces
Describing solid friction by coefficients of friction
EXAMPLE: A piece of wood with a coin on it is raised on one end until the coin just begins to slip. The angle the wood makes with the horizontal is θ = 15°. What is the coefficient of static friction?
θ = 15°
∑Fy = 0
∑Fx = 0
x
y
FBD, coin
Notes: © 2006 By Timothy K. Lund

## Slide 39
Describing solid friction by coefficients of friction
EXAMPLE: Now suppose the plank of wood is long enough so that you can lower it to the point that the coin keeps slipping, but no longer accelerates (v = 0). If this new angle is 12°, what is the coefficient of dynamic friction?
θ = 12°
∑Fy = 0
∑Fx = 0
Topic 2: Mechanics 2.2 – Forces
x
y
FBD, coin
Notes: © 2006 By Timothy K. Lund

## Slide 40: Topic 2: Mechanics 2.2 – Forces
EXAMPLE: A 100. N crate is to be dragged across the floor by an applied force F = 60 N, as shown. The coefficients of static and dynamic friction are 0.75 and 0.60, respectively. What is the acceleration of the crate?
SOLUTION:
Solving problems involving forces and resultant force
FBD, crate
x
y
30°
FYI Since friction is proportional to the normal force, be aware of problems where an applied force changes the normal force.
F
30°
Notes: © 2006 By Timothy K. Lund

## Slide 41: Topic 2: Mechanics 2.2 – Forces
SOLUTION:
Determine if the crate even moves.
Thus, find the maximum value of the static friction, and compare it to the horizontal applied force:
Solving problems involving forces and resultant force
FH =
The maximum static friction force is
Fs,max =
The normal force is found from...
F
mg
N
Ff
a
FBD, crate
x
y
30°
Notes: © 2006 By Timothy K. Lund

## Slide 42: Topic 2: Mechanics 2.2 – Forces
EXAMPLE: If someone gives the crate a small push (of how much?) it will “break” loose. What will its acceleration be then?
SOLUTION:
Solving problems involving forces and resultant force
The dynamic friction force is
Fd = μd N
The reaction force is still N =
The horizontal applied force is still
Thus Fd =
The crate will accelerate.
F
mg
N
Ff
a
FBD, crate
x
y
30°
Notes: © 2006 By Timothy K. Lund

## Slide 43: Topic 2: Mechanics 2.2 – Forces
Newton’s laws of motion – The third law
In words ____________________________________ ____________________________________________
In symbols
In the big picture, if every force in the universe has a reaction force that is equal and opposite, the sum of all the forces in the whole universe is zero!
FAB is the force on body A by body B.
FBA is the force on body B by body A.
Newton’s third law
So why are there accelerations all around us?
Notes: © 2006 By Timothy K. Lund

## Slide 44: Topic 2: Mechanics 2.2 – Forces
Each body acts in response only to the force acting on it.
Identifying force pairs in context of Newton’s third law
EXAMPLE: When you push on a door with 10 N, the door pushes you back with exactly the same 10 N, but in the opposite direction. Why does the door move, and not you?
SOLUTION: Even though the forces are equal and opposite, they are ____________________________.
A
B
FAB
A
FBA
the door’s reaction
your
action
Notes: © 2006 By Timothy K. Lund

## Slide 45: Topic 2: Mechanics 2.2 – Forces
Identifying force pairs in context of Newton’s third law
EXAMPLE:
Consider a baseball resting on a tabletop. Discuss each of the forces acting on the baseball, and the associated reaction force.
SOLUTION:
FEB
FBE
NBT
NTB
Notes: © 2006 By Timothy K. Lund

## Slide 46: Topic 2: Mechanics 2.2 – Forces
Identifying force pairs in context of Newton’s third law
We define a _________________________________ ____________________________________________.
EXAMPLE: Three billiard balls interacting on a pool table constitute a system.
The _______________________________________ ____________________________________________.
For any ____________________________________!
Notes: © 2006 By Timothy K. Lund

## Slide 47: Topic 2: Mechanics 2.2 – Forces
Identifying force pairs in context of Newton’s third law
We define a system as a collection of more than one body, mutually interacting with each other.
EXAMPLE: Three colliding billiard balls constitute a system. Discuss all of the internal forces.
The internal force pairs only exist while the balls are in contact with one another.
Note that a blue force and a red force act on the white ball. The white ball responds only to those two forces.
Note that a single white force acts on the red ball. The red ball responds only to that single force.
Note that a single white force acts on the blue ball. The blue ball responds only to that single force.
Notes: © 2006 By Timothy K. Lund

## Slide 48: Topic 2: Mechanics 2.2 – Forces
Identifying force pairs in context of Newton’s third law
We define a system as a collection of more than one body, mutually interacting with each other.
EXAMPLE: Three billiard balls interacting on a pool table constitute a system. Describe the external forces.
_________________________________________________________________________ (not each other).
For billiard balls, these forces are the _________, the _________________, and the ___________________.
Notes: © 2006 By Timothy K. Lund