THIS IS A PRACTICE ASSESSMENT. Show formulas, substitutions, answers (in spaces provided) and units!

A carbon-core resistor consists of a carbon rod having a length of 8.75 mm, a diameter of  0.0250 mm and a resistivity of 3500(10-8 ( m.

1.	What is the value of the cross-sectional area of the carbon rod.  Be sure your answer is in m2.

1. _________________

2.	What is the resistance of the carbon rod?					2. _________________

3.	If a current of 1.75 A passes through the resistor, what is the voltage across the resistor?

3. _________________

An unknown material has the V-I characteristics shown in the graph.

4.	What is the resistance of the material when the current is 0.2 mA?		4. _________________

5.	What is the resistance of the material when the current is 0.7 mA?		5. _________________

6.	What is the resistance of the material when the voltage is 1.2 V?		6. _________________

7.	Is this material ohmic? Explain. ________. _________________________________________.

A voltmeter records the displayed potential difference when the leads are placed across a 2200 ( resistor.

8.	What is the current passing through the resistor?		8. _________________

9.	How much charge passes through the resistor in exactly 1.5 minutes?

9. _________________

10.	How much electrical energy is required to pass the charge you found in (8) through the resistor?

10. ________________

11.	What is the fractional error in the voltage measurement?			11. ________________

A filament lamp has a rating of 1.50 W. While the bulb is lit, the meter displays the value shown.

12.	What is the power dissipation of the lamp? 	     12. ________________

13.	What is the current in the lamp?		     13. ________________

14.	What is the resistance of the lamp?		     14. ________________

A series circuit powered by a 3.0 V cell is shown.

15.	What is the total or equivalent resistance of this circuit?		          15. ________________

16.	What is the current through this circuit?					16. ________________

17.	What are the voltages across each resistor? 					17. V1 = _____________

V2 = ____________

V3 = ____________

A parallel circuit powered by a 6.0 V cell is shown.

18.	What is the total or equivalent resistance of this circuit?

18. ________________

19.	What is the current through the cell?	19. ________________

20.	What are the currents through each resistor? 				20. I1 = _____________

I2 = _____________

I3 = _____________

21.	What is the current through the point X?					21. ________________

A series circuit powered by a battery whose voltage is 6.0 V is shown in the schematic diagram.

22.	Label VOUT and VIN in this circuit.			22. __In diagram___

23.	Suppose the value of R1 is 2400 (. If we would like to “tap” 1.5 V at VOUT what should the value of R2 be?			23. ______________

24.	Suppose the value of R2 is 2400 (. If we would like to “tap” 1.5 V at VOUT what should the value of R1 be?			24. ______________

25.	What is this type of circuit called?		25. _____________________

A circuit constructed of resistors and two voltage sources is shown.

26.	Use Kirchhoff’s rule for I and write the current equations for each junction.		    26. _____________________

27.	Use Kirchhoff’s rule for V and write the voltage equation for Loop X. 			    27. _____________________

28.	Use Kirchhoff’s rule for V and write the voltage equation for Loop Y. 			    28. _____________________

29.	Find the values of the three currents and the four resistor voltages. Write them in the diagram.

# Text boxes

X

Loop X

Loop Y