## Slide 1: Topic 5: Electricity and magnetism 5.3 – Electric cells
Essential idea: Electric cells allow us to store energy in a chemical form.
Nature of science: Long-term risks: Scientists need to balance the research into electric cells that can store energy with greater energy density to provide longer device lifetimes with the long-term risks associated with the disposal of the chemicals involved when batteries are discarded.
Notes: © 2014 By Timothy K. Lund

## Slide 2: Topic 5: Electricity and magnetism 5.3 – Electric cells
Understandings:
• Cells
• Internal resistance
• Secondary cells
• Terminal potential difference
• Electromotive force (emf)
Notes: © 2014 By Timothy K. Lund

## Slide 3: Topic 5: Electricity and magnetism 5.3 – Electric cells
Applications and skills:
• Investigating practical electric cells (both primary and secondary)
• Describing the discharge characteristic of a simple cell (variation of terminal potential difference with time)
• Identifying the direction of current flow required to recharge a cell
• Determining internal resistance experimentally
• Solving problems involving emf, internal resistance and other electrical quantities
Notes: © 2014 By Timothy K. Lund

## Slide 4: Topic 5: Electricity and magnetism 5.3 – Electric cells
Guidance:
• Students should recognize that the terminal potential difference of a typical practical electric cell loses its initial value quickly, has a stable and constant value for most of its lifetime, followed by a rapid decrease to zero as the cell discharges completely
Data booklet reference:
•  = I ( R + r )
Notes: © 2014 By Timothy K. Lund

## Slide 5: Topic 5: Electricity and magnetism 5.3 – Electric cells
International-mindedness:
• Battery storage is important to society for use in areas such as portable devices, transportation options and back-up power supplies for medical facilities
Theory of knowledge:
• Battery storage is seen as useful to society despite the potential environmental issues surrounding their disposal. Should scientists be held morally responsible for the long-term consequences of their inventions and discoveries?
Utilization:
• The chemistry of electric cells (see Chemistry sub-topics 9.2 and C.6)
Notes: © 2014 By Timothy K. Lund

## Slide 6
Cells
To make a chemical cell, or a battery, you can begin with a container of weak acid, and two electrodes made of different metals.
Different metals dissolve in acids at different rates.
When a metal dissolves, it enters the acid as a positive ion, leaving behind an electron.
We call the weak acid the electrolyte. We call the least negative metal the positive terminal. We call the most negative metal the negative terminal.
Weak Acid
-
-
-
-
-
-
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
+
+
+
+
+
Electrolyte
(+)
(-)
The chemical cell
Topic 5: Electricity and magnetism 5.3 – Electric cells
Notes: © 2014 By Timothy K. Lund

## Slide 7: Topic 5: Electricity and magnetism 5.3 – Electric cells
FYI
Why do the electrons run from (-) to (+) in the external circuit instead of the reverse?
Cells
Think of a chemical cell as a device that converts chemical energy into electrical energy.
If we connect conductors and a light bulb to the (+) and the (-) terminals, we see that electrons begin to flow in an electric current.
-
-
-
-
-
-
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
+
+
+
+
+
Electrolyte
The chemical cell
-
+
(+)
(-)
Notes: © 2014 By Timothy K. Lund

## Slide 8: Topic 5: Electricity and magnetism 5.3 – Electric cells
Cells – primary and secondary
Each time an electron leaves the (-), the acid creates another electron.
Each time an electron enters the (+), the acid neutralizes an electron.
This process is maintained until one of the metals or the electrolyte is completely used up.
A primary cell can’t be recharged.
A secondary cell can be recharged by applying an external voltage, reversing the chemical reaction.
-
-
-
-
-
-
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
+
+
+
+
+
Electrolyte
The chemical cell
-
+
(+)
(-)
Notes: © 2014 By Timothy K. Lund

## Slide 9
PRACTICE: A current isn’t really just one electron moving through a circuit. It is in reality more like a chain of them, each one shoving the next through the circuit. Recalling the charge law “like charges repel, and unlike charges attract,” explain why the current flows from (-) to (+) in terms of the force of repulsion.
SOLUTION:
Consider electrons at A and B.
Both electrons feel a repulsive force at their respective electrodes.
Cells – current
-
-
-
-
-
-
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
+
+
+
+
+
Electrolyte
The chemical cell
-
+
A
B
Topic 5: Electricity and magnetism 5.3 – Electric cells
(+)
(-)
Notes: © 2014 By Timothy K. Lund

## Slide 10
PRACTICE: A current isn’t really just one electron moving through a circuit. It is in reality more like a chain of them, each one shoving the next through the circuit. Recalling the charge law “like charges repel, and unlike charges attract,” explain why the current flows from (-) to (+) in terms of the force of repulsion.
SOLUTION:
But A’s is bigger than B’s because there are more negatives repelling at A than B. Thus A wins.
Cells – current
-
-
-
-
-
-
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
+
+
+
+
+
Electrolyte
The chemical cell
-
+
A
B
Topic 5: Electricity and magnetism 5.3 – Electric cells
(+)
(-)
Notes: © 2014 By Timothy K. Lund

## Slide 11: Topic 5: Electricity and magnetism 5.3 – Electric cells
PRACTICE: Consider electrons at points A and B. Which one has more potential energy?
SOLUTION:
The electron at B has already traveled through the circuit and is returning to the cell so it can do no more work on the bulb.
The electron at A still has the full circuit to travel and can thus still do work on the bulb.
Thus the electron at A has more potential energy.
Cells – electric potential energy
-
-
-
-
-
-
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
+
+
+
+
+
Electrolyte
The chemical cell
-
+
A
B
(+)
(-)
Notes: © 2014 By Timothy K. Lund

## Slide 12: Topic 5: Electricity and magnetism 5.3 – Electric cells
Cells – conventional current
Back in the days of Ben Franklin scientists understood that there were two types of electricity: positive and negative.
What they didn’t know was which one was actually free to travel through a circuit.
The influential Ben Franklin guessed wrongly that it was the positive charge.
Thus, his vision of our chemical cell looked like the one on the next slide.
-
-
-
-
-
-
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
+
+
+
+
+
Electrolyte
The chemical cell
-
+
(+)
(-)
Notes: © 2014 By Timothy K. Lund

## Slide 13: Topic 5: Electricity and magnetism 5.3 – Electric cells
Cells – conventional current
FYI
Positive charge flow is called conventional current and is still used in circuit analysis.
-
-
-
-
-
-
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
+
+
+
+
+
Electrolyte
The chemical cell
-
+
-
-
-
-
-
-
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
+
+
+
+
+
Electrolyte
Franklin’s chemical cell
-
+
less negative
= more positive
more negative
= less positive
(+)
(-)
(+)
(-)
We will use only conventional current in this course.
Notes: © 2014 By Timothy K. Lund

## Slide 14: Topic 5: Electricity and magnetism 5.3 – Electric cells
PRACTICE: Consider positive charges at points A and B. Which one has more potential energy?
SOLUTION:
The charge at B has already traveled through the circuit and is returning to the battery so it can do no more work on the bulb.
The charge at A still has the full circuit to travel and can thus still do work on the bulb.
Thus the positive charge at A has more potential energy.
Cells – electric potential energy
-
-
-
-
-
-
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
+
+
+
+
+
Electrolyte
Franklin’s chemical cell
-
+
A
B
(+)
(-)
Notes: © 2014 By Timothy K. Lund

## Slide 15: Topic 5: Electricity and magnetism 5.3 – Electric cells
FYI Electric potential difference is often abbreviated p.d.
Cells – electric potential difference
We define the electric potential difference as the amount of work done in moving a positive charge q from a point of lower potential energy to a point of higher potential energy.
The units for electric potential difference are volts V or, as can be seen from the formula, J C-1.
-
-
-
-
-
-
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
+
+
+
+
+
Electrolyte
-
+
potential difference
(+)
(-)
Notes: © 2014 By Timothy K. Lund

## Slide 16: Topic 5: Electricity and magnetism 5.3 – Electric cells
Cells – electric potential difference
Think of a battery as an engine that uses chemical energy to take positive charges and move them from low to high potential within the cell so that they can do work outside the cell in the external circuit.
The schematic symbol for a switch is shown.
For this circuit we have the schematic:
Electrolyte
-
+
high potential
low potential
Chemical energy
cell
lamp
switch
(+)
(-)
(+)
(-)
Notes: © 2014 By Timothy K. Lund

## Slide 17: Topic 5: Electricity and magnetism 5.3 – Electric cells
Cells – electric potential difference
As an analogy to gravitational potential energy, think of the chemical cell as an elevator, powered by a chemical engine.
Inside the cell, positive charges at low potential are raised through chemical energy to high potential.
Outside the cell, positive charges at high potential are released into the external circuit to do their electrical work, losing energy as they go.
external circuit
chemical cell
(-)
(+)
Notes: © 2014 By Timothy K. Lund

## Slide 18: Topic 5: Electricity and magnetism 5.3 – Electric cells
FYI
Note the increase rather than the decrease.
Cells – electric potential difference
EXAMPLE:
200 C of charge is brought from an electric potential of 2.0 V to an electric potential of 14 V through use of a car battery. What is the change in potential energy of the charge?
SOLUTION:
From we see that . Thus
J.
Notes: © 2014 By Timothy K. Lund

## Slide 19: Topic 5: Electricity and magnetism 5.3 – Electric cells
Cells – electromotive force (emf)
The electromotive force  (or emf) of a cell is the amount of chemical energy converted to electrical energy per unit charge.
Since energy per unit charge is volts, emf is measured in volts.
This cell has an emf of  = 1.6 V.
Because the cell is not connected to any circuit we say that it is unloaded.
01.6
00.0
Notes: © 2014 By Timothy K. Lund

## Slide 20: Topic 5: Electricity and magnetism 5.3 – Electric cells
EXAMPLE: How much chemical energy is converted to electrical energy by the cell if a charge of 15 C is drawn by the voltmeter?
SOLUTION:
From we have .
Thus
J.
Cells – electromotive force (emf)
01.6
Notes: © 2014 By Timothy K. Lund

## Slide 21: Topic 5: Electricity and magnetism 5.3 – Electric cells
Cells – internal resistance
If we connect a resistor as part of an external circuit, we see that the voltage read by the meter goes down a little bit.
We say that the cell is loaded because there is a resistor connected externally in a circuit.
This cell has a loaded potential difference (p.d.) of V = 1.5 V.
01.5
01.6
Notes: © 2014 By Timothy K. Lund

## Slide 22: Topic 5: Electricity and magnetism 5.3 – Electric cells
Cells – internal resistance
All cells and batteries have limits as to how rapidly the chemical reactions can maintain the voltage.
There is an internal resistance r associated with a cell or a battery which causes the cell’s voltage to drop when there is an external demand for the cell’s electrical energy.
The best cells will have small internal resistances.
The internal resistance of a cell is why a battery becomes hot if there is a high demand for current from an external circuit.
Cell heat will be produced at the rate given by
cell heat rate
= cell internal resistance
Notes: © 2014 By Timothy K. Lund

## Slide 23: Topic 5: Electricity and magnetism 5.3 – Electric cells
FYI
If you double the current, the rate of heat generation will quadruple because of the dependency.
If you accidentally “short circuit” a battery, the battery may even heat up enough to leak or explode!
PRACTICE: A battery has an internal resistance of r = 1.25 . What is its rate of heat production if it is supplying an external circuit with a current of I = 2.00 A?
SOLUTION:
Rate of heat production is power.

 J s-1 ( W.)
Cells – internal resistance
Notes: © 2014 By Timothy K. Lund

## Slide 24: Topic 5: Electricity and magnetism 5.3 – Electric cells
Cells – internal resistance
If we wish to consider the internal resistance of a cell, we can use the cell and the resistor symbols together, like this:
And we may enclose the whole cell in a box of some sort to show that it is one unit.
Suppose we connect our cell with its internal resistance r to an external circuit consisting of a single resistor of value R.
All of the chemical energy from the battery is being consumed by the internal resistance r and the external load represented by the resistance R.

r
R

r
Notes: © 2014 By Timothy K. Lund

## Slide 25
Topic 5: Electricity and magnetism 5.3 – Electric cells
Cells – internal resistance
From EP = qV we can deduce that the electrical energy being created by the cell is EP = q.
The electrical energy being converted to heat energy by R is EP,R = qVR.
The electrical energy being converted to heat energy by r is EP,r = qVr.
From conservation of energy EP = EP,R + EP,r so that q = qVR + qVr.
Note that the current I is the same everywhere.
From Ohm’s law VR = IR and Vr = Ir so that  = IR + Ir.
 = IR + Ir = I(R + r)
emf relationship
Notes: © 2014 By Timothy K. Lund

## Slide 26: Topic 5: Electricity and magnetism 5.3 – Electric cells
EXAMPLE:
A cell has an unloaded voltage of 1.6 V and a loaded voltage of 1.5 V when a 330  resistor is connected as shown.
Find . (b) Find I.
(c) Find the cell’s internal resistance.
SOLUTION:
(a) From the first schematic we see that V. (Unloaded cell.)
(b) From the second diagram we see that the voltage across the 330  resistor is 1.5 V. (Loaded cell.)
so that and A.
Cells – internal resistance
1.6 V
1.5 V
Notes: © 2014 By Timothy K. Lund

## Slide 27: Topic 5: Electricity and magnetism 5.3 – Electric cells
EXAMPLE: (Continued…)
A cell has an unloaded voltage of 1.6 V and a loaded voltage of 1.5 V when a 330  resistor is connected as shown.
(c) Find the cell’s internal resistance.
SOLUTION:
(c) Use the emf relationship .
Cells – internal resistance
1.6 V
1.5 V
Notes: © 2014 By Timothy K. Lund

## Slide 28: Topic 5: Electricity and magnetism 5.3 – Electric cells
EXAMPLE:
A cell has an unloaded voltage of 1.6 V and a loaded voltage of 1.5 V when a 330  resistor is connected as shown.
(d) What is the terminal potential difference t.b.d. of the cell?
SOLUTION:
(d) The terminal potential difference is the potential difference at the terminals of the cell where it connects to the external circuit.
This cell has an unloaded t.p.d of 1.6 V, and a loaded t.p.d. of 1.5 V. Note that the t.p.d. depends on the load.
Cells – terminal potential difference
1.6 V
1.5 V
Notes: © 2014 By Timothy K. Lund